## Slide 1: 9-1-1 DDoS:
Threat, Analysis and Mitigation

## Slide 2: DDoS on 9-1-1
9-1-1 emergency service: allows anonymized call
Requires all carriers to transmit 911 calls to special end point without subscribers validation
Don’t require SIM to make a 911 call
Therefore, it’s possible to launch a DDoS

## Slide 3: Mobile phone botnets
Malware installed in smartphone, normally very stealthy
Make calls without notice of device owner
Steal personal information

## Slide 4: Cellular Network
IMSI (Internal Mobile Subscriber Identity)
  Unique identification number across all cellular networks
  Usage: identify subscriber
  15 digit stored in SIM
IMEI (International Mobile Station Equipment Identity)
  Identifying mobile equipment
  Stored in firmware/burned into ROM
  Required in authentication phase

## Slide 5: Cellular Network
NSI (Non-Service Initialized)
  Register and unregister process
  Basically, your device isn’t connected into network
Emergency Calls
  The “emergency” button in your lock screen
  CM_SERVICE_REQUEST: indicate this is an emergency call
  At least require an IMEI
  Can be made even under NSI

## Slide 6: E911
PSAP (Public-Safety Answering Point)
  Centers that handle 911 calls
Selective Router (SR)
  Special telephony switches used to connect 911 calls to PSAP
Telephone Switch (TS)
  Process of a call being connected to PSAP

## Slide 7: E911
Caller Identification and Location Information
  Used to retrieve caller information
Call Routing
  A 911 call is received
  Transfer the call to local SR
    If no available SR, the call is dropped or transferred to alternative SR
  SR connect the call to PSAP
    If no available PSAP or no available call taker, the call is transferred or dropped

## Slide 8: Several kinds of attack bots
NA (non-anonymized)
  Ordinary smartphone infected with an OS level malware
Anonymized (A)
  Hide IMSI when making the call
  Virtually entering no-SIM state
Persistent Anonymized (A*)
  Bot that ramdomized IMEI or IMSI
  The most stealthy one

## Slide 9: Implementation of NA bot
Launched from OS level
A proxy between RILD and RIL
  RIL: Radio Interface Layer, the interface between low level hardware and high level telephony service
  RILD: Radio Interface Layer Daemon, interface between telephony service and RIL
The proxy send some fake command in owner’s part
Injecting audio into the outgoing call (only certain model)

## Slide 10: Implementation of A bot
Cellular protocol stack:
  managed by a separate real-time OS (RTOS)
  Interacting with Android
Our goal: switch protocol stack into no-SIM mode
Implement a rootkit inside firmware
  Can manage RTOS’s state machine
  Fool the phone!
How to do this? OsmocomBB

## Slide 11: Implementation of A bot
Layered protocol stack
  L1: radio interface
  L2: data link layer
  L3: RR (lowest)-MM(IMEI and IMSI are handled)-CM
Since we can manipulate RTOS’s state machine now
  Initiate 911 call
  Mask IMSI and IMEI before they reach upper layer
  The device is in psudo no-SIM state now

## Slide 12: Implementation of A bot
OsmocomBB
  The only way to freely research the implementation of a mobile’s baseband software
Architecture of the bot
  Caller
  Anonymizer
Caller: handle state machine
  Build emergency call request via MM and CR layer
Anonymizer
  Masking IMEI/IMSI

## Slide 13: Implementation of A bot
Normal register process
Switch on
IMSI attach
Validation
request contains IMSI and location register
Authentication
Carrier sends authentication request to mobile
Answer with encrypted message
Finished register

## Slide 14: Implementation of A bot
Anonymize process
Initialize a SIM card missing report
Invoke flag MMR_NREG_REQ
Detached from network
No SIM card, can still make memrgency calls

## Slide 15: Implementation of A* bot
Detect smartphone’s status (If owner is press the key?)
Detach SIM (Same as A bot)
Set a random IMEI number
  IMEI and/or IMSI are spoofed
Initialize 911 call repeatly

## Slide 16: Implementation of A* bot
A* bot anonymizer
Same as A bot with no-sim state but added IMEI spoofing
Randomized during location update procedure
Each call with a new IMSI
Can’t be blocked!

## Slide 17: Experiment
Test Environment
  A base transceiver station
  Wireshark capturing traffic
Build a simulated model of E911 system based on NC, Charlotte

## Slide 18: E911 Network Simulation
Robustness
  Heavy-tail degree distribution
  Robust to random failures
SR redundancy
  83% PSAPs are connected to single SR
  Highly risky!
Traffic overflows
  No enough call takers

## Slide 19: E911 Network Simulation
PSAP workload
  Yes, you can get busy signal even in an real emergency situation
PSAP call balancing
  No such resources
PSAP call waiting
  Calls can be held

## Slide 20: Attack simulation
Time
  The peak hours
Call Event Generation
Call processing time
  Time for saying “9-1-1, what’s your emergency?”
Redial
  How many people will call again?
SR capacity

## Slide 21: Attack simulation results
Callers who give up

## Slide 22: Attack simulation results
More bots, more legimate calls
Callers are desperately redialing

## Slide 23: Attack simulation results
Network performance
  87% SR overloaded
  Affection 98% callers
PSAP performance
  Wireline: 75% calls affected
  Wireless: 91% calls affected
  Why?

## Slide 24: Countermeasures
Disallow NSI calls?
Trusted Device identification?
Human presence detection?
Call firewall?

## Slide 25: Afterthoughts
Critical challenge
Ethical problem
Wide range regulation change (government, manufacturer, carrier)